## Slide 1: Midterm Project
ITI516 영상처리

## Slide 2: Objective
Implement and test a JPEG encoder and decoder
Observe and report the results
  Check the results of each encoding step
  Visualize the DCT coefficients
  Compute the performance in different Quality Factors
  Compare the results with OpenCV

## Slide 3: Encoding steps (ignore header and Huffman table)
Read an image in grayscale
Process 3-8 for each 8x8 sub-images (blocks)
Shift the intensity level
Forward Discrete Cosine Transform
Quantize
Scan in zigzag order
Run-length encoding
Huffman coding

## Slide 4: Decoding steps (inverse steps of Encoding)
Huffman decoding on the data
Deconstruct RLE
Re-order in zigzag order
Dequantize
Inverse Discrete Cosine Transform
Shift the intensity level
Merge the 8x8 sub-images (blocks)
Compare with the original image

## Slide 5: 5. Quantize
Standard quantization matrix (StdQT)
np.array([
16, 11, 10, 16, 24, 40, 51, 61, \
12, 12, 14, 19, 26, 58, 60, 55, \
14, 13, 16, 24, 40, 57, 69, 56, \
14, 17, 22, 29, 51, 87, 80, 62, \
18, 22, 37, 56, 68, 109, 103, 77, \
24, 35, 55, 64, 81, 104, 113, 92, \
49, 64, 78, 87, 103, 121, 120, 101, \
72, 92, 95, 98, 112, 100, 103, 99
], dtype=int).reshape([BLOCK_SIZE, BLOCK_SIZE])
Quantization table (QT)
* QF: Quality factor
QS: Quality scale
StdQT: Standard quantization matrix
QT: Quantization table
(= Z @p.58 course_05)
.

## Slide 6: 6. Scan in zigzag order
ZIGZAG ORDER
np.array([
0,1,8,16,9,2,3,10, \
17,24,32,25,18,11,4,5, \
12,19,26,33,40,48,41,34, \
27,20,13,6,7,14,21,28, \
35,42,49,56,57,50,43,36, \
29,22,15,23,30,37,44,51, \
58,59,52,45,38,31,39,46, \
53,60,61,54,47,55,62,63
])

## Slide 7: 7. RLE
DC components
  dDC[i] = DC[i] – DC[i-1] if i > 0 else dDC[i] = DC[i]
  Code (size=int(dDC[i]).bit_length(), value=dDC[i])
AC components
  Code (#zeros to skip, size) (non-zero value)
  “EOB” (End-of-Block) denoted by (0, 0)

## Slide 8: 8. Huffman coding
DC components
  dDC[i] = DC[i] – DC[i-1] if i > 0 else dDC[i] = DC[i]
  Code (size=int(dDC[i]).bit_length(), value=dDC[i])
AC components
  Code (#zeros to skip, size) (non-zero value)
  “EOB” (End-of-Block) denoted by (0, 0)
  Symbol: (#zeros to skip, size)

## Slide 9: Example 8.17 @p.56 in course_05

## Slide 10: Compute the performance
PSNR (Peak Signal-to-noise Ratio)
  ,
    where is an original image, and is a compressed image
Compression ratio
    where , are the number of bits in two representations
  Let is (8 bits per pixel the number of whole pixels)
  Measure by counting of binary (coded) data

## Slide 11: Test sub-image
subimg = np.array([
[ 36, 36, 32, 48, 64, 111, 139, 140],
[ 37, 44, 35, 60, 71, 146, 189, 180],
[ 51, 65, 48, 83, 74, 134, 175, 160],
[ 47, 40, 41, 107, 73, 132, 172, 160],
[ 63, 56, 61, 140, 66, 133, 170, 160],
[ 74, 71, 86, 155, 61, 136, 169, 149],
[ 54, 63, 100, 168, 67, 131, 144, 150],
[ 25, 37, 72, 121, 54, 78, 131, 135]
])

## Slide 12: Submission
Submit a PDF file (report)
  File name: ITI516_studentID_name.pdf
  (ex. ITI516_2023021185_이경헌.pdf)
Report should include the results of below:
  Our codes (Screenshots or typings)
  Results of DCT, Quantization, and E.C. for the test sub-image
  Visualize the DCT coefficients for “lena.png”
  Performance (PSNR and Compression ratio) of yours and OpenCV for “lena.png” and “kodim21.png” in QF = {1, 5, 32, 75}
Delay policy
  After the deadline, only 80% per day is accepted.
  After 7 days from the deadline, 0 points.
Due: 29th APR, 18:00